Sperical Intersection Algorithm

The problem is to find the intersection of two paths on the globe, defined as parametric equations of the (possibly approximate) distance along the path from an initial point. The parametric equations give both the position of the point and the slope. We start with a first approximation of the two distances to the intersection point along each line, d1 and d2, which give us the initial points pt1 and pt2.
The basic algorithm is to approximate the path as a great circle tangent to the paths at the initial approximations, pt1 and pt2, as shown in Drawing 1. The distance d1' = pt1 - pt3, so the new approximation for the intersection is therefore result of the parametric function at d1 + d1', and similarly for pt2
Drawing 1: Approximation of Intersection
The problem, therefore, becomes that of finding the distances from pt1 and pt2 to the intersection at pt3. On the plane this is simple, but a planar approximation using latitude and longitude behaves badly around the poles. Therefore spherical trigonometry is used instead.
Drawing 2: Intersection on a Sphere
The point N is the North Pole. Lines lat1 and lat2 are the lines of longitude from N down to pt1 and pt2. Therefore the angle θ0 is the difference in longitude between pt1 and pt2.